## Slide 1: Lagopus handson
NTT Network Innovation lab
version 0.5
Last Update : 01/18/2016

## Slide 2: Today’s Goal
Install and set up OpenFlow switch (Lagopus) and OpenFlow controller (Ryu) in your virtual machine
Run sample application
Target PC (Server/VM)
Ryu
Lagopus
OpenFlow
DPDK
Step1
Step2
nic
nic
Run lagopus on mininet
#mininet: SDN-based network emulation tool

## Slide 3
Preparation for Installing Lagopus and Ryu

## Slide 4: Which do you choice as a target system ?
1. Bare metal
  Bare metal system (PC or server)
    You must choice the DPDK available hardware
  2. Virtual machine
  You must choice the DPDK available virtual
  hardware
Server
OS
Lagopus
Ryu
Server
Linux
Lagopus
Ryu
KVM
Linux
Server
Windows/OS X
Lagopus
Ryu
VMware
Linux
2. Virtual machine
VM

## Slide 5: 1. Bare metal system requirements
#1: http://www.intel.com/content/dam/www/public/us/en/documents/presentation/dpdk-packet-processing-ia-overview-presentation.pdf
Notice: We can not guarantee the complete combination of hardwares.
CPU
Size
  >= 1Gbytes
Memory
Type
  It is better that 64-bit instruction is available.
  The latest Intel CPUs are better
  #A little old cpu may be supported because DPDK is
  available from 2009 year(#1).
  Code Name
  Broadwell/Haswell/Ivy Bridge/Sandy Bridge/Nehalem
Cores
  >= 2 CPU cores
Server
OS
Lagopus
Ryu

## Slide 6: 1. Bare metal system requirements
Notice: We can not guarantee the complete combination of hardwares.
Network Interface Card (NIC)
  Supported network drivers in DPDK
    e1000
  82540, 82545, 82546
    e1000e
  82571-82574, 82583, ICH8-ICH10, PCH-PCH2
    Igb
  82575..82576, 82580, I210, I211, I350, I354, DH89xx
    Ixgbe
  82598..82599, X540, X550
    I40e
  X710, XL710
    Fm10k
  The number of NICs
  >= 3 (2 NICs for Lagopus, 1 NIC for management)
Server
OS
Lagopus
Ryu

## Slide 7: 1. Bare metal system requirements
Notice: We can not guarantee the complete combination of hardwares.
Server
OS
Lagopus
Ryu
Operating system
  Supported OS in DPDK
#Operation checked OS
- Ubuntu 14.04 LTS/Ubuntu 12/04 LTS
- Cent OS 6.5
- Linux
- Free BSD
>= lagopus version 0.2

## Slide 8: 2. Virtual machine requirements
  Type
    Some CPU flags may be set on booting VM. (The next page shows the instruction to specify such CPU flags)
  Cores
    >= 2 cores
  Size
    >= 1Gbytes
Notice: We can not guarantee the complete combination of hardwares.
vCPU
vMemory
Server
Linux
Lagopus
Ryu
KVM
Linux
Server
Windows/OS X
Lagopus
Ryu
VMware
Linux
VM

## Slide 9: 2. Virtual machine requirements
vNIC
  e1000 device
  #KVM/Vmware supports e1000 virtual device
Server
Linux
Lagopus
Ryu
KVM
Linux
Server
Windows/OS X
Lagopus
Ryu
VMware
Linux
VM

## Slide 10: 2. Virtual machine requirements
Sample Vmware Fusion configuration on OS X.
ethernet0.present = "TRUE"
ethernet0.connectionType = "bridged"
ethernet0.virtualDev = "e1000"
ethernet0.wakeOnPcktRcv = "FALSE"
ethernet0.addressType = "generated"
ethernet0.linkStatePropagation.enable = "TRUE"
ethernet0.generatedAddress = "00:0c:29:67:06:91"
ethernet0.pciSlotNumber = "33"
ethernet0.generatedAddressOffset = "0"
ethernet1.present = "TRUE"
ethernet1.connectionType = "hostonly"
ethernet1.virtualDev = "e1000"
ethernet1.wakeOnPcktRcv = "FALSE"
ethernet1.addressType = "generated"
ethernet1.linkStatePropagation.enable = "TRUE"
ethernet1.generatedAddress = "00:0c:29:67:06:9b"
ethernet1.generatedAddressOffset = "10"
ethernet1.pciSlotNumber = "37"
ethernet2.present = "TRUE"
ethernet2.connectionType = "hostonly"
ethernet2.virtualDev = "e1000"
ethernet2.wakeOnPcktRcv = "FALSE"
ethernet2.addressType = "generated"
ethernet2.linkStatePropagation.enable = "TRUE"
ethernet2.generatedAddress = "00:0c:29:67:06:a5"
ethernet2.generatedAddressOffset = "20"
ethernet2.pciSlotNumber = "38”
for Lagopus
vNIC0
vNIC1
vNIC2
for management
vNIC
virtualDev=“e1000”

## Slide 11: 2. Virtual machine requirements
OS
  Supported OS in DPDK
#Operation checked OS
- Ubuntu 14.04 LTS/Ubuntu 12/04 LTS
- Cent OS 6.5
- Linux
Server
Linux
Lagopus
Ryu
KVM
OS
Server
Windows/OS X
Lagopus
Ryu
VMware
OS
VM

## Slide 12
Handson Start!
  1: Install Lagopus
  2: Install Ryu
  3: Run Lagopus with Ryu

## Slide 13
Handson Start!
  1: Install Lagopus
  2: Install Ryu
  3: Run Lagopus with Ryu

## Slide 14: 1: Install Lagopus
Environment
Server
OS
Lagopus
Ryu
Hypervisor
OS
VM
Ubuntu 14.04 LTS
Version 0.2.3
Version 3.26
DPDK
Version 2.0.0

## Slide 15: 1: Install Lagopus
You must move to your home directory
Download lagopus and Intel DPDK
  $sudo apt-get git
  $git clone https://github.com/lagopus/lagopus
  Download “Lagopus”
  Download “Intel DPDK”
  $wget http://dpdk.org/browse/dpdk/snapshot/dpdk-2.0.0.zip
  $unzip dpdk-2.0.0.zip
Need unzip(sudo apt-get install unzip)

## Slide 16: Setup essential software packages
  $ sudo apt-get update
  $ sudo apt-get install make gcc git build-essential libxpat-dev libgmp-dev libssl-dev libpcap-dev byacc flex python-dev python-pastedeploy python-paste python-twisted python-setuptools python-pip libxml2-dev libxslt-dev
  1: Install Lagopus

## Slide 17: Setup essential software packages
  1: Install Lagopus
Make
gcc
Git
build-essential
libxpat-dev
libgmp-dev
libssl-dev
libpcap-dev
byacc
10. Flex
11. python-dev
12. python-pastedeploy
13. python-paste
14. python-twisted
15. python-setuptools
16. python-pip
17. libxml2-dev
18. libxslt-dev

## Slide 18
  1: Install Lagopus
Setup intel DPDK
Compile DPDK libraries
  $ cd ~/dpdk-2.0.0
  $ cd tools
  $ ./setup.sh
:
[30] Exit Script
Option:9
[9] x86_64-native-linuxapp-gcc
For DPDK version

## Slide 19
  1: Install Lagopus
Setup intel DPDK
Loading kernel module
[12] Insert IGB UIO module
:
[30] Exit Script
Option:12
[14] Insert KNI module
:
[30] Exit Script
Option:14
For DPDK version

## Slide 20
  1: Install Lagopus
Setup intel DPDK
[15] Setup hugepage mappings for non-NUMA systems
:
[30] Exit Script
Option:15
Setup hugepages
Input the number of 2MB pages
Example: to have 128MB of hugepages available, enter '64' to
reserve 64 * 2MB pages
Number of pages:256
For DPDK version

## Slide 21
  1: Install Lagopus
Setup intel DPDK
[18] Bind Ethernet device to IGB UIO module
:
[30] Exit Script
Option:18
Bind NiCs to DPDK
Network devices using kernel driver
===================================
0000:03:00.0 '82545EM Gigabit Ethernet Controller (Copper)' if=eth10 drv=e1000 unused=
0000:03:00.1 '82545EM Gigabit Ethernet Controller (Copper)' if=eth11 drv=e1000 unused=
0000:05:00.0 '82545EM Gigabit Ethernet Controller (Copper)' if=eth12 drv=e1000 unused=
0000:05:00.1 '82545EM Gigabit Ethernet Controller (Copper)' if=eth13 drv=e1000 unused=
0000:07:00.0 '82545EM Gigabit Ethernet Controller (Copper)' if=eth0 drv=igb unused= *Active*
Other network devices
=====================
<none>
Enter PCI address of device to bind to IGB UIO driver:eth10
You must choice 2 NiCs
For DPDK version

## Slide 22
  1: Install Lagopus
Compile
  $ cd lagopus
  $ ./configure
  $ make
Install
  $ sudo make install
For DPDK version

## Slide 23
  1: Install Lagopus
Compile
  $ cd lagopus
  $ ./configure –-disable-dpdk
  $ make
Install
  $ sudo make install

## Slide 24
Handson Start!
  1: Install Lagopus
  2: Install Ryu
  3: Run Lagopus with Ryu

## Slide 25
  2: Install Ryu
  $ sudo pip install ryu
  $ sudo pip install six –-upgrade
Notes:   $ sudo pip install stevedore -upgrade

## Slide 26
Handson Start!
  1: Install Lagopus
  2: Install Ryu
  3: Run Lagopus with Ryu

## Slide 27
  3: Run lagopus with Ryu
OpenFlowスイッチがどのくらいOpenFlowの仕様に準拠しているかテスト
するためのツール
Ryu Certification
  $cd /usr/local/lib/python2.7/dist-packages/ryu/tests/switch
  $ ryu-manager --test-switch-dir of13 tester.py
http://osrg.github.io/ryu-book/ja/html/

## Slide 28
veth0
veth2
veth4
veth1
veth3
veth5
br01
br02
VM
Lagopus
Ryu
Setup Lagopus configuration file
  3: Run lagopus with Ryu
Created topology

## Slide 29
$sudo ip link add veth0 type veth peer name veth1
$sudo ip link add veth2 type veth peer name veth3
$sudo ip link add veth4 type veth peer name veth5
$sudo ip link set veth0 up
$sudo ip link set veth1 up
$sudo ip link set veth2 up
$sudo ip link set veth3 up
$sudo ip link set veth4 up
$sudo ip link set veth5 up
Setup network namespace
  3: Run lagopus with Ryu
$ git clone https://github.com/lagopus/handson
$ cd handson
$ ./setup_rawsocket.sh

## Slide 30
  3: Run lagopus with Ryu
Setup Lagopus configuration file
  $ cd /usr/local/etc/
  $ mkdir lagopus
  $ sudo cp ~lagopus/misc/examples/lagopus.dsl /usr/
  local/etc/lagopus/
  $ sudo vi/usr/local/etc/lagopus/lagopus.dsl
  $ mkdir /usr/local/etc/lagopus
  $ git clone https://github.com/lagopus/handson
  $ cd handson
  $ cp lagopus.dsl /usr/local/etc/lagopus/

## Slide 31
  3: Run lagopus with Ryu
Setup Lagopus configuration file
Lagopus.dsl
Network namespaceを活用
channel channel01 create -dst-addr 127.0.0.1 -protocol tcp
channel channel02 create -dst-addr 127.0.0.1 -protocol tcp
controller controller01 create -channel channel01 -role equal -connection-type main
controller controller02 create -channel channel02 -role equal -connection-type main
interface interface01 create -type ethernet-dpdk-phy -port-number0
interface interface02 create -type ethernet-dpdk-phy -port-number1
interface interface03 create -type ethernet-dpdk-phy -port-number2
interface interface04 create -type ethernet-dpdk-phy -port-number3
interface interface05 create -type ethernet-dpdk-phy -port-number4
interface interface06 create -type ethernet-dpdk-phy -port-number5
port port01 create -interface interface01
port port02 create -interface interface02
port port03 create -interface interface03
port port04 create -interface interface04
port port05 create -interface interface05
port port06 create -interface interface06
bridge bridge01 create -controller controller01 -port port01 1 -port port03 2 -port port05 3 -dpid 0x1
bridge bridge02 create -controller controller02 -port port02 1 -port port04 2 -port port06 3 -dpid 0x2
bridge bridge01 enable
bridge bridge02 enable
For DPDK version

## Slide 32
  3: Run lagopus with Ryu
Setup Lagopus configuration file
Lagopus.dsl
Network namespaceを活用
channel channel01 create -dst-addr 127.0.0.1 -protocol tcp
channel channel02 create -dst-addr 127.0.0.1 -protocol tcp
controller controller01 create -channel channel01 -role equal -connection-type main
controller controller02 create -channel channel02 -role equal -connection-type main
interface interface01 create -type ethernet-rawsock -device veth0
interface interface02 create -type ethernet-rawsock -device veth1
interface interface03 create -type ethernet-rawsock -device veth2
interface interface04 create -type ethernet-rawsock -device veth3
interface interface05 create -type ethernet-rawsock -device veth4
interface interface06 create -type ethernet-rawsock -device veth5
port port01 create -interface interface01
port port02 create -interface interface02
port port03 create -interface interface03
port port04 create -interface interface04
port port05 create -interface interface05
port port06 create -interface interface06
bridge bridge01 create -controller controller01 -port port01 1 -port port03 2 -port port05 3 -dpid 0x1
bridge bridge02 create -controller controller02 -port port02 1 -port port04 2 -port port06 3 -dpid 0x2
bridge bridge01 enable
bridge bridge02 enable

## Slide 33
  $ sudo lagopus -d -- -c3 -n1 --vdev eth_pipe0 --vdev eth_pipe1 --vdev eth_pipe2 -- -p3f --core-assign balance
  3: Run lagopus with Ryu
Run Lagopus
  Options
    -d: Debug mode (foreground)
    -c bitmask: Which CPU cores to use
    -n channels: Memory channels
    -p bitmask: Number of port
    -l filename: Specify a log file path (default:syslog)
For DPDK version

## Slide 34
  $ sudo lagopus –d
  3: Run lagopus with Ryu
Run Lagopus
Options
  -d : Debug mode (foreground)
  -l filename: Specify a log file path (default:syslog)

## Slide 35
https://osrg.github.io/ryu-certification/switch/lagopus

## Slide 36
  Further information
より高速にお使いいただくために
gcc4.X, ixgbeを利用する場合
  $ sudo vi dpdk-2.0.0/config/common_linuxapp
CONFIG_RTE_LIBRTE_IXGBE_PF_DISABLE_STRIP_CRC=n
CONFIG_RTE_LIBRTE_IXGBE_RX_ALLOW_BULK_ALLOC=y
CONFIG_RTE_IXGBE_INC_VECTOR=n
CONFIG_RTE_IXGBE_RX_OLFLAGS_ENABLE=y

## Slide 37
  Further information
Lagopusの状態を確認する
  $ lagosh
$lagosh> Show flow #フロー/フローの統計情報の表示
$lagosh> Show bridge #ブリッジの情報/ブリッジの統計情報の表示
$lagosh> Show controller
$lagosh> Show meter
$lagosh> Show group
各種情報の表示
:
その他
  $ lagosh> Configure
  Configure# edit #.dslの内容を書き換えたり..
  $ lagosh> stop #Lagopusを停止します
:

## Slide 38
  Appendix: Install by Ansible
Setup
  $ sudo apt-get install git ansible
  $ git clone https://github.com/lagopus/lagopus-tools
  $ cd lagopus-tools/ansible
  $ echo “[target]” > inventories/hosts_setup
  $ echo “127.0.0.1” >> inventories/hosts_setup
  $ echo “work_dir: /home/lagopus” > playbooks/vars.yml
  $ echo “user: lagopus” >> playbooks/vars.yml
  $ ansible-playbook -i inventories/hosts_setup playbooks/setup.yml -K --connection local

## Slide 39
  Appendix: mininet
Setup
  $ git clone https://github.com/lagopus/mininet
  $ cd mininet
  $ git checkout lagopus
  $ ./util/install.sh -n
Sample
  $ ryu-manager /usr/local/lib/python2.7/dist-packages/ryu/app/simple_switch_13.py
  $ sudo ~/mininet/examples/simplelagopus.py
Reference
  http://openvswitch.org/support/ovscon2015/16/1305-lantz.pdf

## Slide 40
Thank you for your attention
This research is a part of the project for “Research and Development of Network Virtualization Technology” supported by the Ministry of Internal Affairs and Communications.